## Slide 1: How Computing Works - Modern Paradigms of Architecture & System 8. Epilogue
Cong Li 李聪
计算如何运作 – 架构与系统的现代范式
8. 尾声

## Slide 2: What We’ve Learned 我们学了什么
Popular science course on computer architecture & systems
计算机架构与系统的科普课程
Several selected paradigms to run workloads faster
一些使工作负载执行更快的精选范式
Let’s use our last practice (Practice 7.4) for a review
让我们用最后一个实践（实践7.4）来进行一次复习

## Slide 3: What Is Practice 7.4 About? 实践7.4做了什么？(1)
Processing several batches of handwritten
ZIP code recognition using the GPU
用GPU进行多批次的手写邮政编码识别
Naturally in the theme of workload offloading
当然是工作负载分担的主题
But it also exhibits the other paradigms
但它也展示了其他的范式

## Slide 4: What Is Practice 7.4 About? 实践7.4做了什么？(2)
Typical GPUs do not work in the double-precision data type
典型的GPU不处理双精度类型数据
The practice works in the single-precision data type
在这个实践中，我们用单精度数据类型
Actually low precision is a common practice in accelerators
事实上，在加速器中低精度属于常规操作

## Slide 5: What Is Practice 7.4 About? 实践7.4做了什么？(3)
GPUs are processors of high parallelism
GPU是高度并行的处理器
Vector processors in GPUs work in
single instruction, multiple data (SIMD)
GPU中的向量处理器以单指令多数据的方式工作
It also accommodates many threads to execute efficiently, here one thread per test sample: data parallelism
同时它能让很多线程高效执行（这里每
个线程处理一个测试数据：数据并行）

## Slide 6: What Is Practice 7.4 About? 实践7.4做了什么？(4)
Well coordinating host & GPUs helps
efficient resource utilization
恰当地协调主控端和GPU有助于有效的资源利用
We pipeline the data preparation on the host & the data processing on the GPU to reduce resource idle time
我们将主控端的数据准备和GPU的数据
处理流水化，降低了资源的闲置时间

## Slide 7: What Is Practice 7.4 About? 实践7.4做了什么？(5)
Within a compute unit, threads in a group effectively use software managed cache to exploit the reuse of data in a training tile
在一个计算单元内，组内线程通过软件管理的缓存，有效利用了一个训练数据分组内的数据重用
In the GPU, similar cadence from different thread groups gives a good opportunity of training data reuse in the global cache
在GPU中，不同的线程分组相似的步调为训练数据在全局缓存中的重用创造了很好的机会

## Slide 8: What Is Practice 7.4 About? 实践7.4做了什么？(6)
Finally, the program is written in Python, & is interpreted during execution
最后，程序是用Python编写的，解释执行
GPUs are operated through the
pre-compiled PyOpenCL library
GPU则是通过预编译的PyOpenCL库操作
The GPU kernel for nearest neighbor
classification is just-in-time compiled
而用于最近邻分类的GPU kernel却是即时编译

## Slide 9: The Paradigms 这些范式
Paradigms Learned 学习到的范式
  Compilation & interpretation 编译与解释
  Parallelism 并行
  Caching 缓存
  Low precision 低精度
  Workload offloading 工作负载分担
They Work Together 它们一起协作
  To deliver performance 以提升性能

## Slide 10: Generalization 推广
In this course we apply the paradigms to
small & simple programs on relatively old systems
在本课程中，我们把这些范式应用于在 相对较旧的系统上运行的小且简单的程序
They’re widely applied in large-scale real world systems
它们在大型的真实世界的系统中广泛应用
We briefly discuss their use in the emerging scenario: large language model (LLM) inference serving
我们简单地探讨他们在大语言
模型推理服务的场景中的应用

## Slide 11: LLM: Deeply Stacked Modules LLM：深度堆叠的模块
Neural network module 神经网络模块
Conversation history + input token(s)
对话历史 + 输入词符号
Neural network module 神经网络模块
Neural network module 神经网络模块
…
One token generated per pass
一轮生成一个词符号
Output token 输出词符号
Continuous passes to generate the response
持续的轮次生成响应

## Slide 12: Workload Offloading 工作负载分担
Neural network computing is dominated by intensive vector & tensor processing
神经网络计算主要是密集的向量和张量处理
Almost all the modules are offloaded to GPUs or AI accelerators for computation
几乎所有的模块都由GPU或AI加速器分担计算

## Slide 13: Low Precision 低精度
LLMs have a large number of parameters, extremely demanding in memory capacity, compute volume, & data transfer volume
LLM有大量的参数，对于内存容量、
计算量和数据传输量有着极高的需求
Low precision is a common practice for LLMs to reduce capacity & transfer volume, & to boost compute throughput
低精度是常规操作，降低容量和传输量，并提升计算吞吐
16-bit data type is the baseline; 8-bit
& 4-bit data types are very common
16位数据类型是底线，8位和4位数据类型非常常见

## Slide 14: Low-Level Parallelism 底层并行
Vector/tensor processing in neural
networks is highly parallel by nature
神经网络中的向量/张量处理天然是高度并行的
SIMD vector/tensor processors become a perfect fit
SIMD的向量/张量处理器成为了一个完美的适配
Multiple thread groups strengthen the data parallelism
基于线程分组的分块增强了数据并行

## Slide 15: Low-Level Caching 底层缓存 (1)
In stacked neural network layers, output of the
current layer is fed as the input to the next layer
在多层堆叠的神经网络中，当前层的输出会成为下一层的输入
Tweaking the compute order & right-sizing the parallelism help cache the output data for locality of input reuse
调整计算顺序并合理规划并行程度有助于 缓存输出数据，以提升输入数据的局部重用

## Slide 16: Low-Level Caching 底层缓存 (2)
Modules in LLMs are dominated by matrix multiplications & multi-head attention operators
LLM的模块主要是矩阵乘法和多头绪注意力算子
They’re demanding in both computation & data access
它们对计算和数据存取的需求都非常高
It’s important to coordinate caching w/ tiling for data reuse to maximize the efficiency
为提升效率，协调缓存和分块以重用数据尤为重要

## Slide 17: Compilation & Interpretation 编译与解释
LLMs are written in Python, but operators are compiled to run on accelerators
LLM用Python编写，但算子则是编译后在加速器上运行
Complex operators are often written in domain-specific languages, & then compiled by domain-specific compilers to generate efficient executables
复杂的算子时常由特定领域的编程语言编写，随后由特定领域的编译器编译，生成高效的可执行代码

## Slide 18: Model-Level Parallelism 模型层面并行 (1)
Even w/ low precision, a single accelerator may not hold the entire LLM, or serve the inference w/ the low latency required
即便使用低精度，单个加速器可能也无法装下整个模型，或者能够以符合要求的低时延完成推理
We then have to parallelize the model execution over multiple accelerators
于是，我们不得不让模型在多个加速器并行执行

## Slide 19: Model-Level Parallelism 模型层面并行 (2)
So-called tensor parallelism: each module partitioned to 2 accelerators for
divide & conquer
所谓张量并行：每个模块被
切分给2个加速器分而治之
Input 输入
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Output 输出
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Accelerator 1
加速器1
Accelerator 2
加速器2

## Slide 20: Model-Level Parallelism 模型层面并行 (2)
Input 输入
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Output 输出
Processing the input, compute throughput & bandwidth doubled
from 2 accelerators
处理一个输入，来自2个加速器的计算吞吐和带宽加倍
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Accelerator 1
加速器1
Accelerator 2
加速器2

## Slide 21: Model-Level Parallelism 模型层面并行 (2)
Input 输入
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Output 输出
Frequent data exchange in each module reduces the overall efficiency
to some extent
频繁地在每个模块中交换数据一定程度降低了整体效率
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Accelerator 1
加速器1
Accelerator 2
加速器2

## Slide 22: Model-Level Parallelism 模型层面并行 (3)
So-called pipeline parallelism: each accelerator takes half of the modules
所谓流水线并行：每个加速器处理一半的模块
Input 输入
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Output 输出
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Accelerator 1
加速器1
Accelerator 2
加速器2

## Slide 23: Model-Level Parallelism 模型层面并行 (3)
Input 输入
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Output 输出
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Accelerator 1
加速器1
Accelerator 2
加速器2
Processing input 1
处理输入1

## Slide 24: Model-Level Parallelism 模型层面并行 (3)
Input 输入
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Output 输出
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Accelerator 1
加速器1
Accelerator 2
加速器2
Processing input 2
处理输入2
Processing input 1
处理输入1
2 inputs processed at the same time by different accelerators
2个输入在同一时刻被2个加速器处理

## Slide 25: Model-Level Parallelism 模型层面并行 (3)
Input 输入
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Output 输出
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Accelerator 1
加速器1
Accelerator 2
加速器2
Processing input 3
处理输入3
Processing input 2
处理输入2

## Slide 26: Model-Level Parallelism 模型层面并行 (3)
Input 输入
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Output 输出
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Accelerator 1
加速器1
Accelerator 2
加速器2
Only one data exchange, overall efficiency higher
只有一次数据交互，
整体效率高

## Slide 27: Model-Level Parallelism 模型层面并行 (3)
Input 输入
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Output 输出
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Accelerator 1
加速器1
Accelerator 2
加速器2
But 1 input processed by 1 accelerator at a time, latency not improved
然而1个输入在同一时刻只被1个加速器处理，时延无法被改善

## Slide 28: Model-Level Parallelism 模型层面并行 (4)
4 accelerators available
有4个加速器时
Input 输入
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Output 输出
Neural network module 神经网络模块
Neural network module 神经网络模块
…
We can go w/ tensor parallelism only
我们能只用张量并行

## Slide 29: Model-Level Parallelism 模型层面并行 (4)
4 accelerators available
有4个加速器时
Input 输入
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Output 输出
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Or pipeline parallelism only
或者只用流水线并行

## Slide 30: Model-Level Parallelism 模型层面并行 (4)
4 accelerators available
有4个加速器时
Input 输入
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Output 输出
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Or even combine tensor parallelism w/ pipeline parallelism
甚至组合张量并
行与流水线并行

## Slide 31: Model-Level Caching 模型层面缓存
Neural network module 神经网络模块
Conversation history + input token(s)
对话历史 + 输入词符号
Neural network module 神经网络模块
Neural network module 神经网络模块
…
Recall the KV cache
回忆一下KV缓存
Output token 输出词符号
Conversation history KV cache
对话历史KV cache
Some compute eliminated
免除了部分计算

## Slide 32: Another Low-Precision Option 另一个低精度选项
Conversation history KV cache
对话历史KV cache
KV cache & compute over it can also use low precision, e.g., 8-bit or even 4-bit data type
KV缓存以及与KV缓存计算也可以是低精度：8位甚至4位数据类型

## Slide 33: Output Processing Pipeline 输出处理流水线
Accelerator
加速器
Host
主控端
Generate a token
生成一个词符号
Convert the token to text & transfer to user
将该词符号转换成文字并发送给用户
At the same time generate the next token
同时生成下一个词符号
Token 词符号

## Slide 34: Cluster-Level Parallelism 集群级别并行
Host 主控端
Accelerator 加速器
Accelerator 加速器
Accelerator 加速器
Accelerator 加速器
1 inference instance serves at most 4 concurrent sessions
1个推理实例最多同时处理4个会话

## Slide 35: Cluster-Level Parallelism 集群级别并行
Host 主控端
Accelerator 加速器
Accelerator 加速器
Accelerator 加速器
Accelerator 加速器
8 concurrent sessions active
8个同时活跃的会话

## Slide 36: Cluster-Level Parallelism 集群级别并行
Host 主控端
Accelerator 加速器
Accelerator 加速器
Accelerator 加速器
Accelerator 加速器
Scale to 2 instances for data parallelism
扩容到2个实例进行数据并行
Host 主控端
Accelerator 加速器
Accelerator 加速器
Accelerator 加速器
Accelerator 加速器

## Slide 37: Cluster-Level Caching 集群级别缓存
Distributed KV Store 分布式KV存储
  Hold KV cache of all the session 保存所有会话的KV缓存
  Connected w/ network 由网络互联
KV Cache of Active Sessions 活跃会话的KV缓存
  Transferred to & cached in accelerator memory 传送至并被缓存于加速器内存中

## Slide 38: Advanced Optimization 进阶优化
KV Cache by Modules KV缓存对应于各模块
  Compute of the current module pipelined w/ transfer of the KV cache of the next module 当前模块的计算和下一个模块的KV缓存传输流水化执行
There are plenty of optimization opportunities in practice
实践中有很多优化的机会

## Slide 39: Just a Popular Science Course 只是一门科普课程 (1)
Never Meant to Be Complete 原本就未计划强调完整性
  Selective course content 选择性的课程内容
    Mentioned only for some important topics 对于一些很重要的内容只是稍作提及
  Deliberate omission, e.g., 刻意省略，例如
    OS kernel vs user-space application 操作系统内核和用户态程序
    Memory management 内存管理
    Interrupt mechanism 中断机制

## Slide 40: Just a Popular Science Course 只是一门科普课程 (2)
Far from Full Depth 远未触及终极深度
  Practices to demonstrate the power of various optimizations 各个实践以展示各种优化的威力
    But not to the extreme 却并非极致优化

## Slide 41: Closing Remarks 结束语
If you’re interested, learn more about architecture & systems
如果你感兴趣，可在架构和系统方面进行更多的学习
Reflect on your learning w/ those paradigms,
& deepen it through practices
用这些范式反思学习到的内容，
并通过实践深化学习到的内容
Continue evolving in the AI era
在AI时代不断提升

## Slide 42: The End